## Slide 1
State diagram
Sequential Circuit Analysis

## Slide 2
Sequential circuit has additional dimension which is time
Combinational logic only depends on current input
Sequential circuit output depends on previous input other than current input
More powerful than combination logic
Able to model condition which can’t be modeled by combinational logic
What is sequential logic

## Slide 3: Example 1: Draw the state diagram for the given circuit
Sequential circuit using D flip flop
Present States:
A and B
Next States:
A+ and B+
Input:
DA, DB, x
Output:
y

## Slide 4
1. Find out the input equations of the flip flop and the output equation
DA = Ax + Bx
DB = A’x
y = (A+B)x’
Example 1: Draw the state diagram for the given circuit

## Slide 5: Example 1: Draw the state diagram for the given circuit
2. Construct the state table according to the flip flop input and output equations
DA = Ax + Bx
DB = A’x
y = (A+B)x’
When A=0, B=0, x=0, DA = 0.0 + 0.0 = 0
DB = 0’.0 = 0
y = (0+0).0’ = 0
When A=0, B=0, x=1, DA = 0.1 + 0.1 = 0
DB = 0’.1 = 1
y = (0+0).1’ = 0
A |  |  | B |  |  | x |  |  |  | DA | DB | y
0 |  |  | 0 |  |  | 0 |  |  |  | 0 | 0 | 0
0 |  |  | 0 |  |  | 1 |  |  |  | 0 | 1 | 0
0 |  |  | 1 |  |  | 0 |  |  |  | 0 | 0 | 1
0 |  |  | 1 |  |  | 1 |  |  |  | 1 | 1 | 0
1 |  |  | 0 |  |  | 0 |  |  |  | 0 | 0 | 1
1 |  |  | 0 |  |  | 1 |  |  |  | 1 | 0 | 0
1 |  |  | 1 |  |  | 0 |  |  |  | 0 | 0 | 1
1 |  |  | 1 |  |  | 1 |  |  |  | 1 | 0 | 0

## Slide 6: Example 1: Draw the state diagram for the given circuit
A+
B+
3. Find out the next states from the flip flop input values
A | B | x |  | DA | DB | y |  | A+ | B+
0 | 0 | 0 |  | 0 | 0 | 0 |  | 0 | 0
0 | 0 | 1 |  | 0 | 1 | 0 |  | 0 | 1
0 | 1 | 0 |  | 0 | 0 | 1 |  | 0 | 0
0 | 1 | 1 |  | 1 | 1 | 0 |  | 1 | 1
1 | 0 | 0 |  | 0 | 0 | 1 |  | 0 | 0
1 | 0 | 1 |  | 1 | 0 | 0 |  | 1 | 0
1 | 1 | 0 |  | 0 | 0 | 1 |  | 0 | 0
1 | 1 | 1 |  | 1 | 0 | 0 |  | 1 | 0
∴ DA = A+
∴ DB = B+
D Flip-flop Truth table

## Slide 7
A | B | x |  | A+ | B+ | y
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 1 |  | 0 | 1 | 0
0 | 1 | 0 |  | 0 | 0 | 1
0 | 1 | 1 |  | 1 | 1 | 0
1 | 0 | 0 |  | 0 | 0 | 1
1 | 0 | 1 |  | 1 | 0 | 0
1 | 1 | 0 |  | 0 | 0 | 1
1 | 1 | 1 |  | 1 | 0 | 0
00
01
11
0/0
0/1
1/0 0/1
1/0
0/1
1/0
1/0
10
State Diagram
4. Draw the state diagram from the state table
Example 1: Draw the state diagram for the given circuit

## Slide 8: Example 2: Draw the state diagram for the given circuit
Sequential circuit using JK flip flop
Present States:
A and B
Next States:
A+ and B+
Input:
JA, KA, JB, KB, x
Sequential circuit using JK flip flop

## Slide 9: Example 2: Draw the state diagram for the given circuit
1. Find out the input equations of the flip flop and the output equation
JA = B KA = Bx’ JB = x’
KB = A xor X

## Slide 10: Example 2: Draw the state diagram for the given circuit
When A=0, B=0, x=0, JA = 0
KA = 0.0’ = 0
JB = 0’ = 1
KB = 0 xor 0 = 0
2. Construct the state table according to the flip flop input and output equations
JA = B KA = Bx’ JB = x’
KB = A xor X
When A=0, B=0, x=1, JA = 0
KA = 0.1’ = 0
JB = 1’ = 0
KB = 0 xor 0 = 0

## Slide 11: Example 2: Draw the state diagram for the given circuit
A | B | x |  | JA | KA | JB | KB |  | A+ | B+
0 | 0 | 0 |  | 0 | 0 | 1 | 0 |  | 0 | 1
0 | 0 | 1 |  | 0 | 0 | 0 | 1 |  | 0 | 0
0 | 1 | 0 |  | 1 | 1 | 1 | 0 |  | 1 | 1
0 | 1 | 1 |  | 1 | 0 | 0 | 1 |  | 1 | 0
1 | 0 | 0 |  | 0 | 0 | 1 | 1 |  | 1 | 1
1 | 0 | 1 |  | 0 | 0 | 0 | 0 |  | 1 | 0
1 | 1 | 0 |  | 1 | 1 | 1 | 1 |  | 0 | 0
1 | 1 | 1 |  | 1 | 0 | 0 | 0 |  | 1 | 1
3. Find out the next states from the flip flop input values
JK Flip-flop Truth table

## Slide 12: Example 2: Draw the state diagram for the given circuit
A | B | x |  | A+ | B+
0 | 0 | 0 |  | 0 | 1
0 | 0 | 1 |  | 0 | 0
0 | 1 | 0 |  | 1 | 1
0 | 1 | 1 |  | 1 | 0
1 | 0 | 0 |  | 1 | 1
1 | 0 | 1 |  | 1 | 0
1 | 1 | 0 |  | 0 | 0
1 | 1 | 1 |  | 1 | 1
00 11
01 10
0
1
0
0 0
State Diagram
4. Draw the state diagram
from the state table
1 1
1